## Slide 1: Software & Hardware Migration for Analog & Digital I/O in Rydberg-Assisted Quantum Engineering of Light Experiment
Ningshun CHEN
Supervised By
Alexei OURJOUMTSEV & Sébastien GARCIA

## Slide 2
Quantum Photonics group
  One principal investigator
  One CNRS researcher
  Two Doctoral students
  Two Master 2 interns
  One Master 1 intern

## Slide 3: The Experiment

## Slide 4: Theoretical Background
Interactions b/w photons
  Rb atoms & Rydberg states
  Optical cavity
Advantages
  Better photon control
  Minimize information loss
  Experimental repeatability
Probe & control beams

## Slide 5: Experimental Setup
Controls & prepares lasers
Hosts the optical cavity

## Slide 6: Hardware
NI PXIe-1078 chassis
Experimental control system

## Slide 7: Software
VITO
Main control of the platform
Home-made LabVIEW program

## Slide 8
Laboratory Virtual Instrument Engineering Workbench — 2015
Design platform & development environment
Block Diagram
Front Panel

## Slide 9
Subscription starting in 2022
Migration to open source alternatives
  Cost reduction
  Development efficiency
  Experimental adaptability
3 Modules of interest
NI PXIe-1078 chassis

## Slide 10: NI PXI-6713 Analog Output
NI-DAQmx instrument driver
Translation from LabVIEW to Python & C
  OnDemand, Finite
Runtime tests :

## Slide 11: NI 6581 Digital I/O & NI 5761 Analog Input
“Smart” modules with FPGAs
Proprietary bottleneck
Replace modules completely

## Slide 12: Replacing NI FPGA Modules

## Slide 13: Digilent Cmod A7-35T as Digital I/O
48 pins built around Xilinx Artix 7 FPGA
  clock source, SRAM, basic I/O, etc
Already used for some experimental control
Can functionally replace a fraction of digital I/O
  More effort is needed
Intro to FPGAs & HDLs

## Slide 14: Red Pitaya STEMlab 125-14 as Analog Input
Single-board computer
  Xilinx SoC (CPU, FPGA)
  125 MS/s I/O
  14-bit ADC & DAC
  ethernet, etc
Default applications
  Alternative for lab equipments
Data acquisition device
  Sufficient memory
  Noise limits
  Discontinuous acquisition

## Slide 15: Experimental Data Acquisition
NI 5761 Analog Input
4 channels · 250 MHz · 2 bytes/Sample · 10 μs/loop · 100 loops = 2 MB
Red Pitaya
2 channels · 120 MHz · 2 bytes/Sample · 10 μs/loop · 100 loops = 0.5 MB
Repeat every 130 ms

## Slide 16: Red Pitaya: Input Data Memory Storage & Extension
512 MB on-board RAM
Methods
  Lock-in+PID with Oscilloscope
  Data Streaming
  Deep Memory Acquisition (DMA)

## Slide 17: Deep Memory Acquisition (DMA)
Variable ADC buffer RAM
  Default : 2 MB
  Max recommended : 412 MB
125 MS/s @ 32-bit resolution
RAM reconfiguration & rebuild
  2 MB → 4 MB
Remote ~ SCPI (Python / MATLAB)
On-board ~ API (Python / C)
Successful test acquisitions

## Slide 18: Homodyne Detection System with Red Pitaya

## Slide 19: Homodyne Detection System with Red Pitaya
Noise

## Slide 20: Homodyne Detection System with Red Pitaya
homodyne
detector
50 Ω resistor
Electronic Noise

## Slide 21: Red Pitaya: Intrinsic Electronic Noise
N = 524,288

## Slide 22: Homodyne Detection System
Electronic Noise
σHDN2 + σRPN2 = (5.31 mV)2
σHDN = 27.88 (mV)2 >> σRPN2 = 0.29 (mV)2

## Slide 23: Homodyne Detection System
Electronic Noise: Bits

## Slide 24: Conclusion
Analog output w. Python / C
Digital I/O w. Digilent Cmod A7-35T
Analog input w. Red Pitaya
  Noise distribution (bitwise resolution)
  Discontinuous acquisition

## Slide 25: Annex

## Slide 26: Lock-in+PID with Oscilloscope Application
Maintains intensity of probe beam
1 IP core dedicated
  165 bytes ~ 1 MB
  Channel A: 0x40110000
  Channel B: 0x40120000

## Slide 27: Methodology
Hardware modification
  4-byte single-channel → dual-channel storage
    4-byte → 2-byte per sample
    16,384 → 131,072 samples
  Per channel (8x more samples)
    0x4012FFFF → 0x4018FFFF
    164 → 8 * 164 bytes
    65 KB → 0.25 MB !!!
Software modification

## Slide 28: Tests
RAM monitor
Sampling one waveform
Original
  ffull = 7629 Hz, Tfull = 131 μs
Extended
  ffull = 954 Hz, Tfull = 1049 μs

## Slide 29: Results
ffull = 7629 Hz, Tfull = 131 μs
ffull = 954 Hz, Tfull = 1049 μs

## Slide 30: Conclusion
Buggy waveform behavior
Front-end decimation
Not practical for DAQ
Lock-in+PID with Oscilloscope Application

## Slide 31: Data Streaming Application

## Slide 32: Tests & Results
Assumption for default allocation
  164 bytes = 65 KB = 32,768 samples (16 bits / sample)
  ffull = 3815 Hz
  125 MS/s

## Slide 33: Tests & Results
Assumption vs. verification
  164 bytes = 65 KB = 32,768 samples → 164/2 bytes = 32 KB = 16,400 samples
  ffull = 3815 Hz → ffull = 7629 Hz
  125 MS/s → 62.5 MS/s

## Slide 34: Conclusion
Sampling rate field is buggy
Issues remain in newest ecosystem
Also not a practical for DAQ
Data Streaming Application

## Slide 35: DMA Code Structure
Configure signal units, decimation, and trigger source and level
Get reserved memory region address and size
Set DMA buffer address and size for each input channel
Continuously acquire data until buffer is full
Read data from buffer
Process and save data to external file

## Slide 36: DMA Tests & Results
2 MB / channel
ffull = 238 Hz